## Slide 1: Sensing as a Service in 6G Perceptive Networks: A Unified Framework for ISAC Resource Allocation
Authors: Fuwang Dong, Fan Liu, Yuanhao Cui, Wei Wang, Kaifeng Han, and Zhiqin Wang
Published in: IEEE Transactions on Wireless Communications
Date of Publication: 10 November 2022

## Slide 2: Table of Contents
Abstract
Background and motivation
Sensing QoS metrics
ISAC resource allocation framework
Optimization and numerical analysis

## Slide 3: Abstract
Background: Sensing as a Service in 6G
  5G-Advanced / 6G: communication + sensing
  Network functions: detect, localize, track
  Perceptive network: sensing + communication
  Enabling technology: ISAC

## Slide 4: Abstract
Sensing Task | QoS Metric
Target Detection | Probability of Detection
Target Localization | Cramer-Rao Bound (CRB)
Target Tracking | Posterior Cramer-Rao Bound (PCRB)
Sensing QoS Metrics for Different Applications
  Detection: probability of detection / false alarm
  Localization: CRB-based accuracy
  Tracking: PCRB-based state estimation
  Key idea: task-specific sensing QoS

## Slide 5: Abstract
Unified ISAC Resource Allocation Framework
  Resources
    Power
    Bandwidth
  Optimization criteria
    Fairness
    Comprehensiveness
  Output: sensing-communication trade-off analysis

## Slide 6: Introduction
Motivation
  Traditional focus: communication QoS
  6G requirement: environment-aware services
  Example applications
    Connected vehicles
    Drone monitoring
    Smart manufacturing
  Current limitation:
    device-based, low-resolution sensing

## Slide 7: Introduction
Perceptive Network and ISAC
  Perceptive network services
    Wireless communication
    Networked sensing
  ISAC role:
    Shared cellular infrastructure
  Sensing functions:
    Detect, Localize, Track
ISAC Concept
BS
User
User
Target
Target
Communication links + Sensing links

## Slide 8: Introduction
Main Gains of ISAC
  Integration gain
    Shared spectrum
    Shared energy
    Shared hardware platforms
  Coordination gain
    Mutual assistance between sensing and communication
  Open issue:
    Sensing QoS is less mature

## Slide 9: Introduction
Localization QoS
  Target parameters
    Time delay
    Angle of arrival
    Range
  Metric:
    CRB
Tracking QoS
  Metric:
    PCRB
Localization Concept
BS
Target
Position from range / angle

## Slide 10: Introduction
Different Sensing QoS Requirements
  High sensing QoS
    Pedestrians
    Fast-moving vehicles
    Safety-critical targets
  Lower sensing QoS
    Static objects
    Low-risk objects
  Allocation principle:
    User-specific S&C needs

## Slide 11: Introduction
Need for Resource Allocation
  More resources:
    Better QoS
  Practical constraint:
    Limited resources
  Key resources:
    Transmit power
    Bandwidth
  Result:
    Service trade-offs
Resource Allocation Concept
Power
Bandwidth
Allocator
Sensing
Comm.
Split scarce resources by QoS priority

## Slide 12: Introduction
Communication Resource Allocation
  Communication rate:
    Power + Bandwidth
  Existing communication RA domains
    OFDM
    LTE-Advanced D2D
    5G network slicing
    NOMA
    Achievable rate
    Spectral efficiency
    Energy efficiency
    Reliability
Sensing Resource Allocation
  Less explored than communication RA
  Also strongly affected by power and bandwidth

## Slide 13: Introduction
ISAC Resource Allocation Gap
  Existing ISAC RA studies
    Radar / information-signal power allocation
    OFDM-ISAC power allocation
  Main limitations
    Scenario-specific formulations
    Power-only focus
  Gap:
    Network-level power + bandwidth allocation
    Existing works do not fully address the trade-off between communication QoS and different sensing QoS metrics.

## Slide 14: Introduction
Motivation of This Work
  Conventional RA trade-offs
    Among communication users
    Among radar / sensing targets
  New ISAC trade-off
    Sensing service vs. communication service
  Challenge:
    Same resource has different value for each service

## Slide 15: Introduction
Considered System Model
  Scenario:
    Single-cell ISAC system
  Base station:
    MIMO BS
  Provided services:
    Communication service
    Device-free sensing service
  Allocation variables:
    Transmit power and bandwidth
  Future work:
    Cooperative multi-cell sensing

## Slide 16: Introduction
Contribution 1: Unified ISAC RA Framework
  General RA framework for 6G perceptive networks
  Service trade-off
    Communication service
    Sensing service
  Supported sensing services
    Target detection
    Target localization
    Target tracking
  User-specific QoS requirements

## Slide 17: Introduction
Sensing Task | QoS Metric
Target Detection | Probability of Detection
Target Localization | Cramér-Rao Bound (CRB)
Target Tracking | Posterior Cramér-Rao Bound (PCRB)
Sensing Task | QoS Metric
Target Detection | 
Target Localization | Cramér-Rao Bound (CRB)
Target Tracking | Posterior Cramér-Rao Bound (PCRB)
Contribution 2 : Sensing QoS Definition
  Task-specific sensing QoS
  Detection
    Probability of detection
    Probability of false alarm
  Localization
    CRB
  Tracking
    PCRB

## Slide 18: Introduction
Tracking QoS
  Metric:
    PCRB
  Target states
    Range
    Angle
    Velocity
    Position
  Closed-loop tracking:
    EKF(Extended Kalman Filter)
Moving-object tracking concept
current
predicted
EKF
Estimate target state over time

## Slide 19: Introduction
Contribution 3: Optimization Approach
  Optimization criteria
    Fairness: balance QoS
    Comprehensiveness: maximize overall performance
  Problem transformation
    Original formulation to convex form
  Solver: Alternative Optimization (AO)

## Slide 20: Introduction
Alternative Optimization Method
  Coupled variables
    Power allocation
    Bandwidth allocation
  AO procedure
    Fix bandwidth to optimize power
    Fix power to optimize bandwidth
    Repeat until convergence

## Slide 21: Introduction
Contribution 4 : Numerical Trade-off Analysis
  Simulation focus
    Sensing vs. communication services
    Trade-offs among users
    Impact of allocation schemes
  Main insight
    Limited power and bandwidth must follow QoS priorities